PSX Hardware timings.

'Work-in-progress'

The following timings have been obtained from a DTL-H2000 board set running on a PC. The code is compiled C++ and uses some of SONY's library routines.

The timer used is the system clock, Root Counter 2.

This system clock ticks approx every 0.03 microseconds.

The horizontal sync. rate is approx 63.56 microseconds in NTSC.

Therefore 2119 (63.56 / 0.03) system clock ticks approx = 1 horizontal scan line.

The reason that the timings are shown in 'scanlines' is that it is easy to see how much the PSX can do relative to the frame update. Later work will show the timings in terms of work-per-frame.

As of this time, the code that is timed consists of:

ClearOTag. A 4096-entry order table is cleared by SONY's library code routines. This is a fixed time.

N * AddPrim. For each Primitive, SONY's library code is called.

DrawOTag. This is a SONY library code routine which signals the hardware to start drawing the Primitives. It is a non-blocking function, meaning that the drawing hardware can run this code in parallel with the main processor, so...

DrawSync. Is called. This waits for the hardware to finish drawing all the Primitives.

Later work:

Ensure that all timing-related code is accurate.

Calculate fixed time taken for hardware-initialization code, such as ClearOTag, reading input devices, etc.

Use linear regression to derive equations for time-per-primitive, e.g.: poly_f4 = 1/150 of a scanline.

Refine timing software to easily add different types of Primitives to the timed code.

Drawing Primitive.	Count.	Scanlines.

Poly_F4			0		8

1		9

110		10

270		11

440		12

610		13

780		14

950		15

1770		20

2440		25

3340		30

Poly_G4			0		8

1		10

133		11

302		12

472		13

641		14

797		15

1736		21

2295		25

3048		30

Poly_FT4			0		8

1		10

135		11

305		12

475		13

646		14

802		15

1732		21

2308		25

3064		30

PolyGT4			0		8

1		10

134		11

304		12

473		13

644		14

803		15

1734		21

2308		25

3063		30